## Slide 1
Sensor Data used for different Event identification
Mtech Interns- ADAS
BigData

## Slide 2
Sensor data to be used:
- RADAR Data
  Advantage - Gives Range, Velocity, Location of target vehicle.
  Disadvantage - Doesn’t identify the type of object
- CAMERA Data
  Advantage - Identifies the vehicle (color, size of the target vehicle etc.)
  - Gives field of view, distance of vehicles from ego-vehicle.
  Disadvantage - can’t determine speed or velocity of vehicle
SHAUNY MACHADO
Event : Ego-Vehicle follows vehicle that is directly in front of ego-vehicle with constant velocity.

## Slide 3
- For more accuracy and reliability , use both RADAR and CAMERA data
RADAR
CAMERA
Sensors of ego-vehicle
Extract
Range
Velocity
Location
Of target vehicle
Extract image or video of ego-vehicle following target vehicle (object detection)
Event Identification
In .csv format, use python
Use Opencv
Tensorflow or caffe
Deep-learning frameworks
Accuracy of the model
Inputs from sensors
Data cleaning (Feature extraction)
Building a ML model

## Slide 4: ATHISH MANOHAR Event: Cross traffic in Highway/City Camera: The video data contain objects like road signs, traffic lights, or moving objects
Environment
Sensor
Camera
Lidar
Radar
Perception
Environmental
Perception
Localization
video
Image
frame
Trained
model
Event
detection
Object
segmentation

## Slide 5: Model is trained with images of cross traffic signs, side view of car, traffic signal and own lane crossing the priority lane Disadvantage: Due to climatic conditions video captured will not be clear
Lidar :
Advantage:
Data collected is accurate and precise
It is not affected by weather condition
Disadvantage
Cannot be used in when there is high reflecting environment
Radar :
used to detect velocity, range and angle of the object present in the environment this sensor data is not useful in detecting the above event
Point
cloud
3D-annotations
Accurate geo-referenced
coordinates
Car surroundings

## Slide 6: SOURAV K C Event : cut in Scenario-highway.
CAMERA
Advantages:
Cameras tracking helps to resolve identification problems where the target vehicle is not visible in single camera.
Could produce a more accurate geometric understanding of the scene. ( 3D locations and velocities, range to each target )
Could cover a wider area so that more target vehicle are available
Disadvantages:
Transmitting video data can require lots of bandwidth on multiple cameras.
More number of image frames will be collected from a single minute video.
Model accuracy is more important.

## Slide 7
2. Radar Sensor
Advantages:
Radar gives the exact location of the vehicle around the Ego Vehicle.
It provides the Distance and Velocity of the vehicles.
Can detect the stationary and moving vehicle in the highway.
Extraction the data from the radar values can be done easily from the
variations happened in the radar dataset.
Disadvantages:
Radar values for different temperatures.
It cannot differentiate between the heavy and small vehicles.

## Slide 8: Block Diagram for Camera
Camera Video
Model with training dataset
Video into image frames
Identification the cut-in events
Feature extraction
of Event
Block Diagram for Radar
Radar sensor data
Model with training dataset
Extraction of cut-in events
Identification of cut-in events
Feature extraction for the event

## Slide 9
SUMANTH S
Event -Acceleration Deceleration and braking
    MECHANISM :
      Uses machine vision algorithm to analyze the environment and detect the conflict.
      ADVANTAGES :
      Easier to install as an aftermarket device.
      The system are expected to operate flawlessly irrespective of weather condition, visibility or road surface quality.
      Maintains constant frame-rate across the field of view.
      Maintains high-resolution in pixels and color across the full width of its field of view.
      DISADVANTAGES :
      limitation similar to the limitation of human vision poorer detection in inclement weather.

## Slide 10
LIDAR :
MECHANISM :
Uses light waves that reflect off object to detected distance between the source and the detected target.
Advantages :
Typically more accurate than radar with fewer misidentification
Unaffected by light level and has better poor weather performance
Better distance estimation
Lidar sensor data requires much less processing than camera video
Disadvantages :
Lack of dynamic information about the detected the target

## Slide 11
RADAR :
MECHANISM :
Uses radio waves that bounce off objects and Doppler effect to measure the velocities of the detected target.
Advantages :
Can directly measures velocities of the sources and the detected target.
Unaffected by light level and has good poor-weather performance
It’s been around for a long time, so well-developed automotive hardware on the market
Disadvantages :
Increased interference from other sources resulting in more frequent misidentification

## Slide 12
Block diagram : CAMERA
Radar/Lidar data
Feature Extraction(Data log )
Model
Event Identification
RADAR/LIDAR:
Environment
Camera
Convert into frames
Video fetch
Event Identification
Scenario/model

## Slide 13
DEEPAK UMESH
Event- Neighbor vehicle lane change
Camera
Advantages:
Helps recognize stationary objects like traffic signs and white lines along with distance information of moving objects(Stereo).
Relatively smaller in size and low cost.
Calibration can be done easily and maintains constant frame rate for its field of view.
Input(Camera)
Feature Extraction(Frames)
Model
Event Identification

## Slide 14
Disadvantages:
Lacks depth information in the scene.
Increases computational complexities.
Fails to meet expectations in different weather conditions.
RADAR:
Input(CAN)
Model
Output
Data Log

## Slide 15
Advantages:
Detects velocity, range and angle of the object accurately.
It is computationally lighter than other sensor technologies and can work in almost all environmental conditions.
RADAR is paired alongside a camera to enhance a more precision detection system.
Disadvantages:
RADAR has a limited field of view.
RADAR normally loses sight of the target vehicle in curves and struggle and may not detect a vehicle at close quarter.
If multiple objects are close to each other, the RADAR sensor may get confused by them as being one large object and return one centroid range(interference).

## Slide 16
camera
Image signal processing
Decoding & buffering Image aggregation
Model
1) Camera
Advantages:
Cameras are the only sensor technology that can capture texture, color and contrast information.
Cameras are the master of classification and texture interpretation.
Unlike both lidar and radar, cameras can see color, making them the best for scene interpretation.
The camera can able to pick up a lot from lane markings to road signs.
Disadvantages:
Environmental conditions can introduce problems.
Difficulty in detecting non- illuminated and varying lighting conditions.
Block Diagram:
Event Detection
NIKHIL DS Event: Ego vehicle makes a Lane change

## Slide 17
LIDAR:
Advantages:
A road marking detector based on threshold method that make possible segment LIDAR point clouds
The reflection can be used to form the virtual image of an object.
Can be used to identify land cover types
Disadvantages:
Ineffective during heavy rain or low hanging clouds.
Degraded at high sun angles and reflections.
Lidar data
Feature extraction
Point cloud
Model training
Event detection

## Slide 18
RADAR:
Data Input
Processed CAN data
Train model
Event Detection
Advantages:
It can give the exact position of an object.
Can be used in an object-detection system that uses radio waves to determine the range and angle of objects.
It is less affected by adverse weather conditions.
Disadvantages:
It can not recognize color of the targets.
It is also difficult to recognize short range target types.